## Slide 1
Switching Circuit & Logic Design
Lecture 15 : Quinn-McCluskey Method

## Slide 2
What we learned ?
Fundamental : PA + PA’ = P(A+A’) = P
Σm(0,1,4,5) = A’B’C’ + A’B’C + AB’C’ + AB’C
= A’B’ (C’ + C) + AB’ (C’+C) = (A’+A)B’ = B’
  Step 1 : Combined two pairs of adjacent terms
  Step 2 : Two terms combined again

## Slide 3
Which terms can be paired ?
If the terms differ in one position
  AB’C + ABC = A(B’+B)C = AC
  AB’CD’ + AB’CD = AB’C(D’+D) = AB’C
  Etc.

## Slide 4
Quine-McCluskey
List all minterms
Arrange all minterms in groups of same numbers of 1’s
Compare each term of the lower index group with every term in the succeeding group.
Combined terms : Original fixed representation with the differing one replaced by a dash (-).
Combine the terms generated in Step 3 in the same fashion.

## Slide 5
Example
F = Σm (0, 1, 6, 7, 8, 9, 13, 14, 15)
Index | MinTerm | Binary
Index 0 | 0 | 0000
Index 1 | 1 8 | 0001 1000
Index 2 | 6 9 | 0110 1001
Index 3 | 7 13 14 | 0111 1101 1110
Index 4 | 15 | 1111

## Slide 6
Example
Column 1 |  | 
Index | MinTerm | Binary
Index 0 | 0 | 0000
Index 1 | 1 8 | 0001 1000
Index 2 | 6 9 | 0110 1001
Index 3 | 7 13 14 | 0111 1101 1110
Index 4 | 15 | 1111
Column 2 |  |  |  | 
Pairs | A | B | C | D
0,1 0,8 | 0 - | 0 0 | 0 0 | - 0
1,9 8,9 | - 1 | 0 0 | 0 0 | 1 -
6,7 6,14 9,13 | 0 - 1 | 1 1 - | 1 1 0 | - 0 1
7,15 14,15 | - 1 | 1 1 | 1 1 | 1 -

## Slide 7
Column 2 |  |  |  | 
Pairs | A | B | C | D
0,1 0,8 | 0 - | 0 0 | 0 0 | - 0
1,9 8,9 | - 1 | 0 0 | 0 0 | 1 -
6,7 6,14 9,13 | 0 - 1 | 1 1 - | 1 1 0 | - 0 1
7,15 14,15 | - 1 | 1 1 | 1 1 | 1 -
Column 3 |  |  |  | 
Quads | A | B | C | D
0,8,1,9 | - | 0 | 0 | -
6,14,7,15 | - | 1 | 1 | -

## Slide 8
Column 2 |  |  |  | 
Pairs | A | B | C | D
0,1 0,8 | 0 - | 0 0 | 0 0 | - 0
1,9 8,9 | - 1 | 0 0 | 0 0 | 1 -
6,7 6,14 9,13 | 0 - 1 | 1 1 - | 1 1 0 | - 0 1
7,15 14,15 | - 1 | 1 1 | 1 1 | 1 -
Column 3 |  |  |  | 
Quads | A | B | C | D
0,8,1,9 | - | 0 | 0 | -
6,14,7,15 | - | 1 | 1 | -

## Slide 9
With K-Map
F = Σm (0, 1, 6, 7, 8, 9, 13, 14, 15)
AB\CD | 00 | 01 | 11 | 10
00 | 1 | 1 |  | 
01 |  |  | 1 | 1
11 |  | 1 | 1 | 1
10 | 1 | 1 |  | 

## Slide 10
Minimise with QM
Σm(6,7,8,9)
+ d(10,11,12,13,14,15)
Index 1 | 8 | 1 | 0 | 0 | 0
Index 2 | 6 | 0 | 1 | 1 | 0
 | 9 | 1 | 0 | 0 | 1
 | 10 | 1 | 0 | 1 | 0
 | 12 | 1 | 1 | 0 | 0
Index 3 | 7 | 0 | 1 | 1 | 1
 | 11 | 1 | 0 | 1 | 1
 | 13 | 1 | 1 | 0 | 1
 | 14 | 1 | 1 | 1 | 0
Index 4 | 15 | 1 | 1 | 1 | 1

## Slide 11
Minimise with QM
Index 1 | 8 | 1 | 0 | 0 | 0
Index 2 | 6 9 10 12 | 0 1 1 1 | 1 0 0 1 | 1 0 1 0 | 0 1 0 0
Index 3 | 7 11 13 14 | 0 1 1 1 | 1 0 1 1 | 1 1 0 1 | 1 1 1 0
Index 4 | 15 | 1 | 1 | 1 | 1