## Slide 1
Switching Circuit & Logic Design
Lecture 20 : Synchronous Circuit

## Slide 2: Synchronous Circuit
Combinational Circuit
Memory Elements
Inputs
Outputs

## Slide 3: Latches and Flip-Flops
Most important memory element is flip-flop

## Slide 4: Latches and Flip-Flops
Most important memory element is flip-flop
Flip-flops are made by an assembly of gates

## Slide 5: Latches and Flip-Flops
Most important memory element is flip-flop
Flip-flops are made by an assembly of gates
Flip-flop has only “TWO” outputs
Q
Q’

## Slide 6: Latches and Flip-Flops
Most important memory element is flip-flop
Flip-flops are made by an assembly of gates
Flip-flop has only “TWO” outputs
Q
Q’
Flip-flop has only “TWO” stable states
“ONE” bit memory

## Slide 7: S-R latch
S
R
Q
Q’
S
R
Q
Q’
S | R | Qn | Qn+1 | State
0 | 0 | 0 | 0 | No Change
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | Reset
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 1 | Set
1 | 0 | 1 | 1 | 
1 | 1 | 0 | x | Indeterminate/Invalid
1 | 1 | 1 | x | 

## Slide 8: S-R Latch with NAND
S
R
Q
Q’

## Slide 9: Flip-Flop
S
R
Q
Q’
CLK
clk | S | R | Qn | Qn+1 | State
1 | 0 | 0 | 0 | 0 | No Change
1 | 0 | 0 | 1 | 1 | 
1 | 0 | 1 | 0 | 0 | Reset
1 | 0 | 1 | 1 | 0 | 
1 | 1 | 0 | 0 | 1 | Set
1 | 1 | 0 | 1 | 1 | 
1 | 1 | 1 | 0 | x | Indeterminate/Invalid
1 | 1 | 1 | 1 | x | 
0 | x | x | 0 | 0 | No Change
0 | x | x | 1 | 1 |